## Slide 1: ADF7024 Low Power, Easy to use, ISM Band Radio
Analog Devices
Jan 2015

## Slide 2: ADF7024 Overview
Easy to use
431 – 435MHz and 862 – 928MHz
FSK and GFSK modulation
Data rates of 9.6, 38.4, 50, 100, 200 and 300 kbps
Packet handling integrated
  Preamble, sync word and cyclic redundancy check (CRC)
  Manchester encoding and decoding
  8b/10b encoding and decoding
  Data whitening and de-whitening
  Integrated VCO, PLL Loop filter and Tx/Rx switch
Smart Wake Modes
  Autonomous packet sniff, carrier sense and packet reception
  Ultra low power
Receiver Specs
  Sensitivity: -111dBm @ 9.6kbps
  Blocking: 76dB @ 10MHz offset
Transmitter Specs
  Output Power: -20 to +13.5dBm
  Phase Noise: -131dBc/Hz @ 2MHz offset
Power Consumption Specs
  Rx: 12.8mA
  Tx: 23.3mA @ 10dBm
  Sleep: 0.33uA

## Slide 3: Applications
Typical Applications
  Wireless sensor networks (WSNs)
  Home and building automation
  Asset tracking
  Process and building control
  Industrial control
  Internet of Things (IoT)
Suitable for operation under these Regulations
  ETSI EN 300-220
  FCC part 15.247
  FCC part 15.249
  FCC part 15.231

## Slide 4: Ease of Use - The ADF7024 Radio Profiles
Radio Profile | Data Rate (kbps) | Modulation | Frequency Deviation (kHz) | IF Bandwidth (kHz) | Typ Channel Spacing (kHz) | RF Frequency Range (MHz) | Typical Receiver Sensitivity (dBm), BER=0.1%
A | 9.6 | FSK/GFSK | 9.6 | 100 | ≥ 150 | 862 – 928 | -111
B | 38.4 | FSK/GFSK | 20 | 100 | ≥ 150 | 431 – 435, 862 - 928 | -107.5
C | 50 | FSK/GFSK | 25 | 100 | ≥ 150 | 862 – 928 | -107.4
D | 100 | FSK/GFSK | 25 | 100 | ≥ 150 | 862 – 928 | -105
E | 200 | FSK/GFSK | 50 | 200 | ≥ 300 | 862 – 928 | -103
F | 300 | FSK/GFSK | 75 | 300 | ≥ 400 | 862 – 928 | -100.5
The ADF7024 supports six radio configurations (radio profiles A to F).
Configuration register settings are provided for each profile so the user does not need to worry about the RF configuration of the ADF7024.
This ensures that the RF communication layer works seamlessly, allowing the user to concentrate on the protocol and system level design and prototyping.
The radio profiles cover common data rates used in ISM band applications.

## Slide 5: Typical Application Circuit

## Slide 6: Packet Management
The ADF7024 automatically handles the Tx and Rx packets – this simplifies the host processor implementation
  240 byte packet buffer
  Automatic insertion and detection of preamble, sync word, and CRC
  Optional Manchester and 8-bit/10-bit data encoding and decoding
  Optional data whitening

## Slide 7: QUICK START GUIDE TO EVALUATING THE ADF7024
ADF7024 Design Package
  A collection of documentation, files and resources to aid in evaluating the ADF7024
  Includes the following:
    ADF7024 Reference Manual
    Schematics, Gerbers and BOMs for the ADF7024 evaluation boards
    Application notes
    IR calibration firmware download
  Download it from: www.analog.com/ADF7024
  (requires registration)
EVAL-ADF7xxxMB4Z
Mother Board
  An evaluation and software development mother board for the ADF7024. This mother board is required for evaluation of the ADF7024 daughter boards.
  The Renesas RL78 microcontroller is the host microcontroller
  The included Evaluation Suite CD installs the following:
    ADF7024 Evaluation GUI
    ADF7024 GUI User Guide
    MB4Z Hardware User Guide
    Example Host Code and projects for the ADF7024
    IAR Embedded Workbench for Renesas RL78 16K Kickstart
  Order it from: www.analog.com/ADF7024
EVAL-ADF7024DBxZ
Radio Boards
  There are four ADF7024 radio daughter board models available for evaluation:
  EVAL-ADF7024DB1Z
    Separate Tx/Rx match
    862 – 928 MHz
  EVAL-ADF7024DB2Z
    Combined Tx/Rx match
    862–928 MHz
  EVAL-ADF7024DB3Z
    Separate Tx/Rx match
    431 – 435 MHz
  EVAL-ADF7024DB4Z
    Combined Tx/Rx match
    431 – 435 MHz
  Order it from: www.analog.com/ADF7024
EngineerZone
  Support for the ADF7024 is provided via the EngineerZone online community.
  Go to: https://ez.analog.com/community/low-power-rf-transceivers

## Slide 8: Comparison vs the ADF7023
The ADF7024 is easier to use, though less flexible in terms of RF configuration than the ADF7023.
Similarities between ADF7024 and ADF7023:
  Same RF Specifications
  Pin compatible
  Very similar register map
  Same SPI protocol
Main differences between ADF7024 and ADF7023
  ADF7024 can only be used under specified radio profiles – makes it much easier to use, though less flexible
  ADF7023 supports OOK modulation, the ADF7024 does not support this
  ADF7023 has a differential PA option, the ADF7024 does not support this
  ADF7023 has option for external 32kHz XTAL, the ADF7024 does not support this
  ADF7023 has support for AES and Reed Solomon encryption firmware downloads, the ADF7024 does not support these downloads
  ADF7023 supports address filtering. ADF7024 does not.